## Slide 1
Mission Readiness & Predictive Maintenance Copilot
From sensor data to mission decision — in one pipeline.
Team KMstra | Track: AI | IBM Bob AI Hackathon
AstraPulse
01

## Slide 2
The
Problem
02
Disconnected Signals
Sensor & HUMS data contains early degradation signals but remains siloed — disconnected from failure risk, RUL estimates, and mission requirements.
Reactive Decisions
Manual, reactive maintenance creates compounding risks: safety incidents, unplanned downtime, and escalating operational costs across mission-critical fleets.
No Readiness Score
Without a unified readiness signal, operators cannot assess true mission readiness — every decision is a guess under pressure with incomplete information.

## Slide 3
03
IsolationForest
Detects anomalies and scores asset health from raw sensor streams. Flags early degradation signals before failure thresholds are reached.
XGBoost
Predicts failure risk probability using engineered features. Classifies assets as Low, Medium, or High risk based on sensor patterns.
RandomForest
Estimates Remaining Useful Life (RUL) in cycles. Provides time-to-failure horizon to inform scheduling and mission planning.
Mission Readiness Score
0–100
Maintenance Priority
4-Tier
Asset Status: READY / ADVISORY / NOT READY
3-Way
The Solution

## Slide 4
04
System
Architecture
  NASA C-MAPSS FD001 raw sensor data → Preprocessing (17 features + RUL labels) → Feature Engineering (85 features) → Train 3 ML Models (IsolationForest, XGBoost, RandomForest) → Readiness Engine → asset_readiness.csv
  Runtime: FastAPI backend → React Mission Intelligence UI. IBM Bob connects via MCP with 5 operator tools for fleet readiness, asset status, time series, maintenance priorities, and mission readiness decisions.
End-to-End Pipeline
View Demo

## Slide 5
05
Live Demo
Walkthrough
Step 1: Upload
Upload multi-cycle CSV from an unseen engine. System validates, cleans data, and engineers 85 features automatically.
Step 2: Assess
POST /api/assess runs 3 ML models: IsolationForest health, XGBoost failure risk, RandomForest RUL on latest engine cycle.
Step 3: Output
Frontend displays Health Score, Failure Risk, RUL, Readiness Status, and maintenance priority in real time.

## Slide 6
IBM Bob
Copilot
06
MCP Tools
5 operator tools via MCP: fleet readiness, asset status, asset time series, maintenance priorities, and mission readiness. Structured context handoff.
Operator Layer
Bob converts ML model outputs into plain-language operator decisions. It is not the predictive model — it interprets and communicates results.
Context Handoff
Structured context from readiness engine is passed to Bob. Each query returns actionable guidance: go/no-go, maintenance urgency, and fleet status.

## Slide 7
07
READY Engines
NOT READY
Health Normal
RUL Healthy
Low Failure Risk
Mean Readiness
Results & Impact
  100 test engines assessed: 70 READY, 10 ADVISORY, 20 NOT READY.
  Mean readiness score: 73.2/100.
  High-risk alerts: ENG-034 and ENG-024 flagged for immediate action.
  Maintenance priorities: 12 immediate, 10 high, 8 medium, 70 low.
  Health distribution: 57 normal, 22 warning, 21 critical.
  Failure risk: 78 low, 4 medium, 18 high. RUL classification: 44 healthy, 56 advisory.
  AstraPulse delivered end-to-end readiness assessment across all 100 unseen engines with zero manual intervention.

## Slide 8
08
Team KMstra
  Vaibhavi Kariya (ML + Integration)
  Pushti Kansara (ML Health)
  Disu Makadiya (ML Failure)
  Rutvi Shah
  Shared Build: NASA C-MAPSS Pipeline · Synthetic Data · 3 ML Models · Readiness Engine · FastAPI + React · IBM Bob MCP · Automated Testing + Frontend + Data
Sensor Data → Health → Failure Risk → RUL → Readiness → Mission Decision